Tuning hosts for network performance
Glen Turner
2008-01-29
Sysadmin miniconf of linux.conf.au
aarnet
Australia's Academic
and Research Network

---
Motivation
Networks are as good as they are going to get
  - Bandwidth is either cheap or non-existent
  - Hardware-based routers forward packets at line rate with no avoidable jitter
  - Latency remains
Yet a user still can't fill a 1Gbps ethernet link of useful length
The reasons for this reside in the host: applications, operating systems, hardware, algorithms

---
Fundamental TCP
aarnet
Australia's Academic
and Research Network

---
TCP ― Transmission control protocol
User's view
  - a connection between applications: multiplexed, reliable and in order, flow controlled
Network designer's view
  - cooperative sharing of link bandwidths
  - avoiding the congestion collapse of the Internet
The genius of TCP is that it uses one mechanism to solve these disparate requirements
  - the windowed Acknnowledgement

---
TCP window, 1 of 2
Every transmitted byte has a sequence number*
Sender
  - track sequence number sent and sequence number acknowleged
  - buffer the sent but un-acknowledged data in case it needs to be retransmitted
* Or with TCP window scaling each 2n of bytes has a sequence number

---
TCP window, 2 of 2
Receiver
  - Buffer incoming segments
  - Ack every second segment or, after a delay, lone segments
  - Implement flow control by lowering the advertised window as receiver buffer is consumed
Retransmission
  - The amount of data to be re-sent is less than the window, since this caused congestion
  - So, maintain a “congestion window”, the bandwidth the sender thinks it can consume without causing congestion

---
Slow start mode
Don't cause congestion collapse with a new connection
  - We have no estimate of the congesting bandwidth
  - Start with one or two segments
  - Double this per round-trip time, ie: exponential
Congestion occurs, ie: an Ack is late
  - Cwnd was increased too much
    - set the slow-start threshold to half the cwnd
    - Resume slow start from previous cwnd until the ssthresh
    - Now enter congestion avoidance mode, a linear approach to the expected congesting bandwidth

---
Congestion avoidance mode
Maintain an existing connection
Increment the congestion window by one cwnd per round-trip time
  - Gives a linear growth in bandwidth
If an Ack is late, reduce cwnd by one segment and re-enter slow start
  - An improvement is to drop back only to ssthresh and have ssthresh lag cwnd
Sensitive to reordered packets
  - so wait for three duplicate Acks if the Ack shows a hole in the transmitted data

---
Properties of the TCP algorithm
Slow start is exponential, but still very slow for high-bandwidth connections
Packet loss during slow start is devastating
Congestion control leads to a sawtooth “hunting” around the congested bandwidth
  - wasting large absolute amount of bandwidth
Loss is interpreted as congestion

---
Host buffer sizing
Both the sender and receiver need to buffer data
  - the sender's unacknowleged data is more critical
Size for both is the bandwidth-delay product of the path
The BDP is easy to compute in general, but difficult for a specific connection
  - requires knowledge of the ISP's networks
  - in general, use the interface bandwidth and a guess at the worst delay, verified with a ping

---
Operating systems
aarnet
Australia's Academic
and Research Network

---
Buffer sizing in Linux, 1 of 2
The kernel tries to autotune the buffer size, up to 4MB
  - calculate the BDP, if under 4MB do nothing
This is fine for ADSL and 802.1g connections in Australia, but too little for gigabit ethernet in Australia
  - it takes 90ms one-way just to cross the Pacific, so the defaults are too low for us

---
Buffer sizing in Linux, 2 of 2
Linux has two sysctls
    - net.ipv4.tcp_rmem
    - net.ipv4.tcp_wmem
These are vectors of <minimum, initial, maximum> memory usage, in bytes
Set the maximum size to the BDP plus a big allowance for kernel data structures
Keep the initial value near the default, as it could be used to DoS your server

---
Applications and buffer sizing
Applications can request a TCP buffer size
  - setsockopt(…, SO_SENDBUF, …)
    setsockopt(…, SO_RECVBUF, …)
These requests are trimmed by
  - net.core.rmem_max
    net.core.wmem_max
Setting the buffer size explicitly disables autotunung
  - iperf always sets the buffer size, so never gives true results for Linuxl. Ouch!

---
Distributions
Some distributions detune the TCP stack, undo that
  - net.ipv4.tcp_moderate_rcvbuf = 1
    net.ipv4.tcp_timestamps = 1
    net.ipv4.tcp_window_scaling = 1
    net.ipv4.tcp_sack = 1 *
    net.ipv4.tcp_ecn = 1 *
    net.ipv4.tcp_syncookies = 1
    net.ipv4.tcp_moderate_rcvbuf = 1
    net.ipv4.tcp_adv_win_scale = 7 *
      - * These parameters trigger bugs in some networking equipment
        SACK – Cisco PIX
        ECN – Cisco PIX
        Window scale > 2 – a number of ADSL gateways

---
TCP algorithm variations
The traditional TCP algorithm has reached its limits
  - All operating systems offer an alternative, Linux offers all the alternatives it legally can
A selection
  - CUBIC. The current default in Linux. Quick slow start, not too much hunting, fairness is poor
  - Westwood+. Tuned for lossy links such as WLANs.
  - Hamilton TCP. Nicely fair.
It is the sender's choice of algorithm which is important

---
MTU – Maximum transmission unit
The largest packet size which can pass down a path
Why?
  - Larger MTUs reduce the packet-handling overhead of the operating system
  - Above 1Gbps the Mathis, et al formula tells us that MTU > 1500 is needed for a single long-distance connection to be able to fill the pipe
IP subnets require all hosts on the subnet to have the same MTU

---
MTU – Ethernet jumbo frame
Not standard, look for
  - 1Gbps jumbo frame: 9000B
  - 10GE super jumbo frame: 64KB

---
Networks and larger MTUs
Use the maximum MTU between network devices
  - Allows 9000 bytes with MPLS and other headers to pass through
  - Aim is to fix the bug with current MTUs visible to hosts and always deliver 9000 bytes to the host adapter
Worthwhile regardless of customer take-up, as gives outstanding improvement to OSPF and BGP convergence

---
Low memory fragmentation
Low memory is used for network and disk buffers
512MB on 32-bit processors
Linux will happily fragment kernel memory, the common case of a network backup server fragments memory in about 2TB and dies in about 6TB with RHEL3 using jumbo frames
Linux 2.6.24 has anti-fragmentation patches
64-bit processors have more low memory

---
iptables
Network performance is hampered when a buffer is copied, conntrack modules do this when parsing a packet
NAT is obviously slow since it has to alter the buffer
So distros which depend on a iptables firewall for security aren't really suitable for speeds ~1Gbps
  - tcpwrapper is still useful

---
Virtualisation
Don't do this at the moment
Eventually there will be little effect but at the moment the effect is large
  - Need interfaces to use zero-copy from host to VM
  - Need host interfaces to have a flow cache to cheaply route packets to VMs

---
Debugging tools
smokeping
tcptraceroute
ttcp
iperf
Web100
wget
NPAD
Kernel has a new netlink API for TCP state changes
Wireshark and passive tap

---
Debugging technique
Use a scientific approach
  - Create a hypothesis
  - Design an experiment to test the hypothesis
  - Repeat
Record results

---
Debugging – the nightmare
Solving network performance issues is hard
  - Lots of things to go wrong
  - Don't have access to every configuration item in the path
  - May not even have information about the path and a end-host
  - Cutting edge of computing knowledge
Made a lot easier if intrumentation of routers and hosts is extensive
  - Conversely, most ISPs can't make graphs public and won't make fault reports public

---
Applications
aarnet
Australia's Academic
and Research Network

---
Latency
Speed of light in fibre decreases 5% per decade, diameter of Earth reduces 7mm per decade
But applications programmers are prolifigate with round-trips
Example: HTTP
  - Fetch web page, be redirected
  - Fetch web page
  - Fetch CSS
  - Fetch images
Example: GridFTP

---
Applications programing
RPCs often hide unneccessary round-trips
The database access methods are really slow
TCP wants to stream data, adding a read/write protocol above this (such as CIFS) slows things terribly
Application acceptance testing should use tc's NetEm module to add a delay to the test network

---
OpenSSH
OpenSSH has its own TCP-like window
  - Which wasn't big enough for transfers from Australia
  - Patch available since 2004, finally integrated in OpenSSH 4.7 in 2007. Shipped in Fedora 8, anticipated in Ubuntu 8.04.
OpenSSH insists on on-the-fly encryption
  - Network transfers can be CPU bound by the single-threaded OpenSSH encryption process
  - Science sensor data is white noise which requires a supercomputer to make sense of, so the value of encryption is?

---
NFS and delayed Acks
NFS sends 8KB blocks using RPC
Across 1500B TCP connections
The protocol sends an odd number of packets, which means that the Ack is delayed for each NFS protocol data unit

---
Networks
aarnet
Australia's Academic
and Research Network

---
Loss
TCP treats loss as congestion and backs off
High loss leads to connections never leaving slow start
The higher the bandwidth the longer recovery from loss takes
Wireless has a high loss, so use wired links where you care about performance
  - A 802.1n WLAN cannot push a ADSL2+ link to capacity because of loss

---
Ethernet nway auto-negotiation
Do me a favour and leave the interface set to autonegotiation. If that doesn't work, throw out the NIC card: this will be cheaper.
Widely misunderstood
  - Disabling negotiation implies you set the other interface to 10Mbps, half duplex
  - The clocking on your UTP interface brings the link speeds equal
  - But the other interface's duplex is still half and this causes loss
Either leave autoneg alone or set both the host and the switch to the same manual parameters

---
Firewalls
Many firewalls are PCs running Linux, so we're simply moving the performance problem
  - An unexpected result of World Domination
Many firewalls have TCP bugs
Firewalls software needs to be kept up to date
  - You would think that they would be, but many firewalls are installed without a plan for non-service effecting software upgrades

---
Acks need bandwidth too
The return path can encounter congestion. If this slows Acks down then this will slow the TCP connection, despite the adequate forward path bandwidth
Actually, just adding jitter to the Acks will effect the RTT variance calculation. A beginner's mistake is to put Acks into a differing QoS class
ADSL links suffer from this, especially if you congest the uplink by hosting services

---
Some paths are bad news
The “European tour” undersea cables (“22 countries in 3 days”) have high loss
Old cable systems have high loss
Copper cables between buildings on a campus have high loss unless grounding is sophisticated
Satelite links have high loss and high latency (about 500ms for geosync up-and-back)
Ensure an optical loss calculation is done for every optical path longer than 2Km
  - SPF output changes with age and temp

---
Ethernet switches
Ethernet switches usually lack adequate buffering, so don't use them for changes in transmission rates
Ethernet switches are tuned for VoIP, not for TCP throughput and fairness.
  - Ask about nerd knobs

---
Host hardware
aarnet
Australia's Academic
and Research Network

---
Validation: a myth
Purchasing hosts for high performance networking has been difficult
  - Motherboards with poor disk controllers
  - Motherboards with near-broken GbE controllers
    - Wouldn't interrupt for received packets until a packet to send is queued
  - Supposedly identical disks which weren't
Impossible to validate the software
  - Really, really want the latest cutting-edge distro and its kernel
  - Web100 and similar patches unsupported
Increased risk for projects with fast networking

---
TCP TOEs
Only useful at particular stages of hardware development
Otherwise causes more problems than it solves, since the TCP stack becomes a black box

---
Linux as a router
aarnet
Australia's Academic
and Research Network

---
Real routers
Have
  - a forwarding plane
  - a control plane
  - an administrative plane
Which operate independently
CPU-based routers combine all these together and have poor isolation
  - excessive forwarding can black-hole routing
  - attacks on the control plane drop the administrative plane
  - no hitless software upgrades

---
Linux as a toy router
Linux does as good a job as any CPU-based router if configured correctly
Buffers
  - Set them to at least 0.25 of the BDP
QoS
  - Implement the typical DSCPs
  - Implement a good queuing discipline
Control protocols
  - Set QoS so control protocols not black holed

---
Services
There is no good open source routing software
  - Quagga, OpenBGP, xorp are adequate
NTP
  - Use the vendor service of pool.ntp.org
Have a online software update strategy
  - Linux is the operating system most responsible for network abuse: its qualities as a network server are as attractive to black hats as to white hats

---
Take home lessons
aarnet
Australia's Academic
and Research Network

---
Lessons
Networking bottlenecks are moving from links and routers to the hosts
Setting buffer memory fixes most performance issues
  - Linux autotuning is getting better all the time
If you have a host which needs serious network performance
  - Move it outside of the firewall
  - Instrument it and its network to the extreme
  - Run a cutting-edge distro with a cutting-edge kernel
    - Fedora, Ubuntu with your own kernel

---
Tuning hosts for network performance
www.gdt.id.au/~gdt/presentations
Glen Turner
glen.turner@aarnet.edu.au
aarnet
Australia's Academic
and Research Network